## Slide 1: TeloTalkie - Digital Audio Transmission
Fabian Fischer, Julian Arnold
17th July 2014

## Slide 2: Introduction
Telosb
Mic Amp
Telosb
Audio Amp

## Slide 3: Introduction
Digital audio transmission between two nodes
Telosb sensor mote
  ADC and DAC
  Normally used with TinyOS
Microphone amplifier
Audio amplifier

## Slide 4: Microphone Amplifier

## Slide 5: Microphone Amplifier
Signals coming from microphone very weak
  OpAmp circuit to boost signal to match ADC input range
  Low pass filter to band limit signal before sampling
  Custom PCB
Remember: Active circuit which resides next to transmitter
  While transmitting large drops in supply voltage
  Disturbed power supply couples into signal path
    Amplified by OpAmp

## Slide 6: Audio Amplifier

## Slide 7: Audio Amplifier
DAC not capable of driving headphones directly
  Use audio OpAmp to deliver enough power
  Interpolation filter required
  Variable gain required
  Custom PCB
Support for headphones and speaker
  Only mono audio

## Slide 8: Software Overview
ADC samples at 10kHz
ADC sample width 12bit
  Required data rate 120kbits/s
Data rate not achievable using TinyOS
  Do not use operating system at all
  Bare-metal programming

## Slide 9: Samples Pipeline
ADC
2x
Buffering
TX
RX
3x
Buffering
DAC
Sender
Receiver

## Slide 10: Samples Pipeline
Tripel Buffering
  At least Double Buffering to prevent underflow
  RF Chip has the capability to send data only when channel is clear
    The time between consecutive received samples is not constant
    We need buffering for under- and overflow
  Supports voice effects/enhancement, which needs computation time

## Slide 11: Conclusion / Future Work
Good quality voice transmission
Interference fee design challenging
Sensor motes pretty constrained
Add better interference immunity
Add voice effects
Implement control protocol

## Slide 12: Questions?